## Slide 1: AI-Powered Cold Storage & Indoor Air Quality Monitoring System
Real-time IoT Telemetry & Predictive Analytics
Presented by:
Nishant Raushan Sharma
Vanisha Raj Tanwar

## Slide 2: Introduction & Background
Cold storages require strict climatic control to prevent spoilage.
Manual monitoring is error-prone and reactive.
Toxic gas leaks pose immense safety and financial risks.
Our Solution: Real-time telemetry via IoT Edge devices and Cloud ML.

## Slide 3: The Core Problem
Lack of Predictive Insights: Alarms only trigger after threshold is crossed.
Data Silos: Hardware alerts fail to notify stakeholders rapidly.
Hardware Limitations: Low-end microcontrollers struggle to run ML.

## Slide 4: Project Objectives
Real-time Synchronization: Sub-second streaming from Edge to Web.
Predictive Hazard Modeling: Machine Learning to classify state.
Scalable Architecture: Python FastAPI & Docker for deployment.
Centralized Dashboard: Live visualizations of sensor data.

## Slide 5: High-Level System Overview
Sensing Edge: ESP32 captures localized environmental data.
Communication Layer: HTTP POST payload over Wi-Fi.
Intelligent Cloud: FastAPI handles ML inference & DB storage.
Presentation Layer: Live dashboard rendering (WebSockets).

## Slide 6: Input Module & Sensors
DHT11 Sensor: Ambient Temperature (°C) & Humidity (%).
MQ-2 Sensor: Detects Smoke and combustible gases.
MQ-135 Sensor: Air Quality (Ammonia, NOX, Benzene, CO2).
Input Flow: Multi-sensor array -> ESP32 API -> JSON Payload.

## Slide 7: Output & Response Module
Hardware Actuators: Relays, LED, and Buzzer alerts.
Live Visualizations: Real-time multi-dimensional charts.
Predictive States: Binary classification (SAFE vs DANGER).
Confidence Metrics: ML probability thresholds displayed dynamically.

## Slide 8: System Architecture
Tier 1 (Perception Layer): ESP32 hardware scanning environment.
Tier 2 (API & ML): FastAPI Web Server + Scikit-Learn Model.
Tier 3 (Client): JavaScript dashboard via WebSockets.
DevOps: SQLite logging, wrapped in Docker, deployed to Railway.

## Slide 9: Methodology & ML Process
Data Synthesis: 17,500 rows of environmental sensor permutations.
Preprocessing: Parameters sized via robust scaling methodology.
Algorithm: Random Forest (Accuracy) / Logistic Regression (Speed).
Inference Pipeline: Raw -> Transformation -> ML Weight Matrix -> Probability.

## Slide 10: Implementation & Tech Stack
Microcontroller: C++ via Arduino IDE, ArduinoJson.
Backend Framework: Python 3, FastAPI, Uvicorn.
ML Stack: Numpy, Pandas, Scikit-Learn.
Frontend / Deployment: HTML5, Chart.js / Docker on Railway.

## Slide 11: Results
Consistent low-latency from hardware detection to global UI.
98.42% predictive AUC accuracy achieved via Random Forest.
Successful real-time plotting of 4 independent sensor streams.

## Slide 12: Key Advantages
Edge-Cloud Synergy: Bypasses ESP32 memory constraints.
Platform Agnostic: Web-based dashboard from any device worldwide.
High Extensibility: Decoupled sensor addition logic.
Cost Effective: Built on affordable hardware and Open Source frameworks.

## Slide 13: Limitations
Network Dependency: If Wi-Fi goes down, cloud predictions halt.
SQLite Constraints: Local DB lacks massive spatial scaling.
Sensor Calibration: MQ sensors require periodic precision tuning.

## Slide 14: Future Scope
TinyML (Edge AI): Native TensorFlow Lite Micro on ESP32.
Enterprise Migration: Transition to managed PostgreSQL clusters.
Computer Vision: Integrate ESP32-CAM for visual degradation analysis.
Alert Integrations: Automated SMS/WhatsApp API warnings.

## Slide 15: Conclusion
Successfully bridged physical hardware with modern cloud AI.
Demonstrated democratization of predictive industrial telemetry.
Produced an end-to-end blueprint for smart cold storage oversight.

## Slide 16: References
Espressif Systems: ESP32 Technical Reference Manual.
Pedregosa et al.: Scikit-learn Machine Learning in Python.
FastAPI & Uvicorn Framework Documentations.
Chart.js Library API references.